## Slide 1: Microcontroller
Atmel ATMega328P

## Slide 2: Features
8 Channel 10-bit ADC
USART
Low power (3.3V)
16MHz system clock
Simple instruction set (RISC)
  131 Instructions
Interrupts & Timers
$9.78 USD ~ $13.50NZD (excl. Shipping)

## Slide 3: Alternative
Texas Instruments MSP430FR4133
  Features:
    Ultra-Low-Power
    UART
    16MHz System Clock
    10 Channel 10-bit ADC
    16KB FRAM (Ferroelectric RAM)
    2KB SRAM
    16-Bit RISC Architecture
    $14USD ~ $20NZD (excl. Shipping, as at 21/08/16)
  IDE:
    Code Composer Studio or IAR Embedded Workbench
  Development Language:
    C

## Slide 4: C Flowchart (LOGIC)
START
END
Set UCSRB to enable UART transmit
Set UCSRC to set asynchronous mode, data frame size, parity and stop bit
Set UBRR to the required baud rate with selected frequency
Prepare data (character) for transmission
Check if UDR empty.
UDRE == 0;
No
Yes
Transmit Character
Need to transmit another character?
No
Yes

## Slide 5: C Flowchart (Code)
START
END
UCSR0B |= (1 << TXEN0);
UCSR0C |= (1 << UCSZ01) | (1 << UCSZ00);
UBRR0H = (unsigned char) (MYUBRR>>8);
UBRR0L = (unsigned char) MYUBRR;
uint8_t digits[] = {0bXXXXXXXX, …};
While(!(1<<UDRE0) && (UCSR0A));
False
True
UDR0 = digits[x]
while(x < sizeof(digits)/sizeof(digits[0]))
False
True